## Slide 1
HOT WATER
LIQUID 2
LIQUID 3
LIQUID 3
16x2 LCD
DISPLAY
BUTTONS
ESP32
Solenoid Valve
Solenoid Valve
Solenoid Valve
Solenoid Valve
PUMP
FLOW
METER
(YF-S402B)
OUTPUT
WASTE WATER
2IN - 1OUT
VALVE

## Slide 2
Solenoid Valve:
https://www.theengineerstore.in/products/12v-half-inch-solenoid-valve?srsltid=AfmBOoqr1g65WkTXUh9ruPyDg3CeFIysmqomQO7kCjLCllkMky44cDog
PUMP:
https://robu.in/product/12v-nkp-dc-s10b-mini-peristaltic-pump/
Component: | Function:
ESP32 | Main controller
Pump (peristaltic/diaphragm) | Dispenses liquid (coffee/milk/tea)
Flow Sensor | Measures exact liquid volume
Solenoid Valve | Controls liquid path to cup (1 output)
Display | Shows menu, quantity, progress
Buttons (tactile) | User selects beverage & quantity

## Slide 3
Dispensing Flow Sequence
User selects beverage & volume on LCD via buttons.
ESP32 opens the corresponding solenoid valve for the selected liquid.
ESP32 turns ON pump.
Flow meter pulses are counted; ESP32 stops pump & closes valve when desired volume is reached.
ESP32 switches 2-in-1 valve to cup (Output).
System optionally flushes remaining liquid to waste before next operation.
Display shows “Done”.

## Slide 4
Coffee Machine Working Principle
The coffee machine operates based on user input provided through buttons. When a user presses a button, the selected option is displayed on the LCD screen.
An ESP32 microcontroller is connected to multiple liquid (LEQ) valves and a water valve. Based on the user’s selection, the ESP32 controls these valves to perform the desired operation.
Example: If the user selects a coffee type that requires LEQ1 (10 ml) and LEQ2 (15 ml), the ESP32 activates the respective pumps and directs each liquid through a flow meter. The flow meter measures the quantity — for every 44 clock pulses, it allows 10 ml of liquid to pass through.
Once the LEQ1 flow is completed, a cleaning cycle is initiated. Water passes through the same path to flush out any remaining liquid and is directed to the waste line. After cleaning, LEQ2 flow begins, ensuring no mixing between different liquids.

## Slide 5
Troubleshooting and Solution
During the testing phase, I faced two main issues:
The I²C line was connected through two extension cables, which caused communication errors between the ESP32 and the connected I²C devices.
The ground (GND) connection between the ESP32 and the peripheral modules was not properly connected, leading to unstable readings and malfunctioning sensors.
Solution:
I resolved the problem by using a single, shorter I²C connection to reduce signal noise and ensure reliable communication. Additionally, I connected all modules to a common ground, which stabilized the entire circuit and restored proper operation of the I²C devices.
Possible Distances i2c
On a PCB (Same Board): Up to 30 cm. This is ideal and very reliable.
With a Cable (Between Boards): Up to 1 meter. This is possible if you use a low speed (100 kHz) and strong pull-up resistors.
With Special Chips (Extenders): Up to 20+ meters. Using an I2C extender or buffer IC makes this possible.

## Slide 6
⚙️ 1️⃣ What issue did you face?
I faced a communication problem in the I²C line because I used two extension cables and missed the ground connection.
⚙️ 2️⃣ How did you identify it?
I checked the I²C scan — no devices were detected. Then I inspected the wiring and found the ground was not connected properly, and the cable was too long.
⚙️ 3️⃣ How did you solve it?
I used a single short I²C cable and connected all devices to a common ground. After that, communication worked perfectly.
⚙️ 4️⃣ What did you learn?
I learned that I²C needs short, stable connections and a proper common ground for reliable communication.
⚙️ 5️⃣ What will you do next time?
I’ll plan wiring properly, check ground continuity first, and test I²C connections early during setup.

## Slide 7
Project: Liquid Mixer System
Developed an ESP32-based automated liquid mixing system using I2C communication and embedded C. Implemented valve and flow-meter control for precise liquid measurement and automatic cleaning to ensure accurate, contamination-free operation.
Tools & Technologies: ESP32 Controller, Embedded C, I2C Communication, Flow Meter, Solenoid Valves, Sensors, LCD Display